## Slide 1
Agriculture IoT
Team 8corn

## Slide 2
CONTENTS
Team AgIoT
Introduction
Feasibility of LoRa versus APRS in AgIoT
Smart Farm using LoRa/APRS & MQTT
QnA

## Slide 3
1
Team 8Corn
Dong Jun (DJ) Kim
Kyunghee Univ.
Miran Lee
Dongguk Univ.
Chaehee(Pearl) Weon
Seoul Women’s Univ.
Heejae(Lydia) Jung
Kyunghee Univ.
Gowoon(Kayla) Choi
Dongguk Univ.
Woojin(Arthur) Jang
Chungang Univ.
Hyuk (Brian) Lee
Handong Univ.
Hye Won(Hazel) Yoon
Kyunghee Univ.
Brandon Long
Purdue Univ.
Zeeshan Khalid
Purdue Univ.
Notes: 학교는 안넣어두대나..?

## Slide 4
2
Introduction
Project Background
Notes: 왜 프로젝트를 하게 됐는지?
--> 40마일 떨어진 농부가 체크하기 위해서 어쩌구저쩌구 (토니 교수님께 ppt 요청)

## Slide 5
Feasibility of LoRa versus APRS in AgIoT

## Slide 6
CONTENTS
Introduction
Design
Result
Conclusion
Future Works
Feasibility
of LoRa versus APRS
in AgIoT

## Slide 7
1
Introduction
LoRa and APRS
Long Range
915 MHz
Low Power Wide Area Network (LPWAN)
Long-range transmissions with low power consumption
( more than 10km in open area )
Notes:   통신속도는 LTE에 기반한 타 규격보다는 느리지만 SigFox나 Zigbee보단 빠른편 X

## Slide 8
1
Introduction
LoRa and APRS
Automatic Packet Reporting System
144.39 MHz
Amateur radio based system for real time
digital communications of immediate value
in the local area

## Slide 9
1
Introduction
LoRa and APRS
IoT

## Slide 10
2
DESIGN
LoRa Circuit
Transmitter
Receiver

## Slide 11
2
DESIGN
APRS
Transmitter
Receiver

## Slide 12
3
Result
Test

## Slide 13
3
Result
Friis transmission equation
Friis transmission equation

## Slide 14
3
Result
Fresnel Zone
Fresnel Zone
=
, )

## Slide 15
Transmitter Power | 24 dBm
Transmitter Gain | 1.17 dBi
Receiver Gain | 7 dBi
Theoretical Distance | 67.1 km ( 41.70 mile )
Height Needed | 186.58m ( 612.14 ft )
3
Result
Test Result
LoRa
APRS
Transmitter Power | 16 dBm
Transmitter Gain | 9 dBi
Receiver Gain | 6 dBi
Theoretical Distance | 9.3 km ( 5.78 mile )
Height Needed | 27.79m ( 91.17 ft )
for distance 0.84 km
antenna height should be 20.88m
for distance 4.2 km
antenna height should be 18.67m
“
“
“
“
Transmitter Antenna Height | 2.1 m ( 6.89 ft )
Receiver Antenna Height | 2.7 m ( 8.86 ft )
Tested Distance | 4.2 km ( 2.6 mile )
Efficiency Constrained by Height | 45.16%
Transmitter Antenna Height | 2.1 m ( 6.89 ft )
Receiver Antenna Height | 3.2 m ( 10.50 ft )
Tested Distance | 0.84 km ( 0.52 mile )
Efficiency Constrained by Height | 1.25%
Notes: theoretical height needed
efficiency constrained by height

## Slide 16
4
Conclusion
Limitation and Conclusion
Transmitter and Receiver place 186m height for 67km coverage distance
by Fresnel Zone
67km
186m
//

## Slide 17
5
Future Works
APRS and LoRa
Test LoRa and APRS distance coverage with same gain antennas
Install antennas on taller structure and test

## Slide 18
Smart Farm using LoRa/APRS & MQTT

## Slide 19
CONTENTS
Introduction
Design
Data & Algorithm
Result
Future Works
Smart Farm using
LoRa/APRS & MQTT

## Slide 20
1
Introduction
Our Part
1. Low-cost
2. Low power consumption
3. High convenience for management
4. Lightweight messaging protocol
5. High reliability
Key Factors of Smart Farm:
Notes: There are several studies on suggesting LoRa as the networking technology for smart farms.

## Slide 21
1
Introduction
MQTT
MQTT is a machine-to-machine (M2M)/"Internet of Things" connectivity protocol.
It was designed as an extremely lightweight publish/subscribe messaging transport.
It is useful for connections with remote locations where a small code footprint is required and/or network bandwidth is at a premium.
“
“
Notes:   통신속도는 LTE에 기반한 타 규격보다는 느리지만 SigFox나 Zigbee보단 빠른편 X

## Slide 22
1
Introduction
Our Part
Irrigation System
: Use wireless to control the sprinklers

## Slide 23
1
Introduction
Our Part
Smart Farm Web Interface
: Checking the status of the farm

## Slide 24
2
DESIGN
Use only edge computing without using cloud
Use MQTT sn over LoRa communication
Send packets by using UDP to TTN(Cloud) & use edge computing
LoRa Try
Use LoRa and MQTT separately

## Slide 25
2
DESIGN
APRS Try
Build APRS Transmitter with Raspberry Pi and HX1
Connect APRS Transmitter using Arduino and HX1 to Raspberry Pi
Use MQTT on APRS network
Use APRS and MQTT separately
Notes: hx1 raspberry pi 위에 올리는 거 실패해서, 아두이노랑 라파 연결함

## Slide 26
2
DESIGN
Arduino Uno
LoRa Shield
Temp & Humidity Sensor
Soil Humidity Sensor
Solenoid valve
High level trigger
Raspberry pi
LoRa Hardware

## Slide 27
2
DESIGN
APRS Hardware
Arduino Uno
Temp & Humidity Sensor
Raspberry pi
Solenoid valve
High level trigger
HX1 transmitter
RTL SDR dongle
Soil Humidity Sensor

## Slide 28
2
DESIGN
LoRa Software

## Slide 29
2
DESIGN
APRS Software

## Slide 30
2
DESIGN
LoRa Diagram
admin

## Slide 31
2
DESIGN
LoRa Diagram

## Slide 32
2
DESIGN
LoRa Diagram

## Slide 33
2
DESIGN
LoRa Diagram

## Slide 34
2
DESIGN
LoRa Diagram

## Slide 35
2
DESIGN
LoRa Diagram

## Slide 36
2
DESIGN
APRS Node Circuit
Node1 – Sensor Package
Node4 – Actuator
Node3 – BROKER
Node2 – GATEWAY
APRS Transmitter
MQTT Broker & MQTT Subscriber & APRS Transmitter
APRS Receiver
APRS Receiver & MQTT Publisher
Notes: 로라도 저 회로도 받아서 추가하깅

## Slide 37
2
DESIGN
APRS Diagram

## Slide 38
2
DESIGN
APRS Diagram

## Slide 39
2
DESIGN
APRS Diagram

## Slide 40
3
Data & Algorithm
Collected Data
Temperature
Soil moisture
Humidity
Weather

## Slide 41
3
Data & Algorithm
Algorithm
Soil Moisture Data
MIN: 0 MAX : 696

## Slide 42
3
Result
LoRa Demo

## Slide 43
3
Result
APRS Demo

## Slide 44
Internet is Needed
Edge Logic is determined only by the Farmer’s manual decision and Soil Moisture
No monitoring system for sensors and nodes
5
Future Works
LoRa
Build without the Internet
Increase the accuracy of the weather prediction
Make sensor monitoring system
Ex) sensor malfunction, battery consumption …

## Slide 45
5
Future Works
APRS
Build APRS transmitter with Raspberry Pi and HX1
> using GPS
> meaning of Broker
Control multi node
Build without the Internet

## Slide 46
QnA

## Slide 47
Thank You !